## Slide 1: Performance
P&H (1.6 thru 1.12)

## Slide 2: Outline
What does performance mean?
What to measure for performance?
  Cycle time
  Clock rate
  CPI
  MIPS
What affects performance?
The power wall
Performance benchmarks (SPEC)
Fallacies and pitfalls

## Slide 3: Which airplane is “best”?
Airplane
Passenger capacity
Cruising range (miles)
Cruising speed (mph)
Passenger throughput (passengers x mph)
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Passenger Capacity | 146 | 132 | 470 | 375
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Cruising Range (miles) | 8720 | 4000 | 4150 | 4630
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Cruising Speed (mph) | 544 | 1350 | 610 | 610

## Slide 4: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?

## Slide 5: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 6: Design Tradeoffs
Performance is rarely the sole factor
  Cost is important too
  Energy/power consumption is often critical
Frequently used compound metrics
  Performance/Cost (throughput/$)
  Performance/Power (throughput/watt)
  Work/Energy (total work done per joule)
    for battery-powered devices

## Slide 7: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 8: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 9: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 10: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 11: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 12: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 13: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 14: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 15: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 16: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 17: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 18: Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency

## Slide 19: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 20: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)

## Slide 21: CINT2006 for Intel Core i7 920

## Slide 22: SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)

## Slide 23: SPECpower_ssj2008 for Xeon X5650

## Slide 24: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
  Can’t be done!
Example: multiply accounts for 80s/100s
  How much improvement in multiply performance to get 5× overall?
Corollary: make the common case fast

## Slide 25: Fallacy: Low Power at Idle
Look back at i7 power benchmark
  At 100% load: 258W
  At 50% load: 170W (66%)
  At 10% load: 121W (47%)
Google data center
  Mostly operates at 10% – 50% load
  At 100% load less than 1% of the time
Consider designing processors to make power proportional to load

## Slide 26: Pitfall: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second
  Doesn’t account for
    Differences in ISAs between computers
    Differences in complexity between instructions
  CPI varies between programs on a given CPU

## Slide 27: Concluding Remarks (P&H Chapter 1)
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance